## Slide 1
Michael J. Neely, University of Southern California
http://www-bcf.usc.edu/~mjneely/
CISS, Princeton University, March 2012
Wireless Peer-to-Peer Scheduling in Mobile Networks
Base Station

## Slide 2
Base Station
Want to increase the throughput in wireless systems.
Current system designs cannot support future mobile traffic.
Ideas:
  Throughput can be significantly increased by allowing
device-to-device communication.
  Exploit file popularity and caching capabilities.
Without Device-to-Device Transmission
(Example Timeslot).

## Slide 3
Base Station
Want to increase the throughput in wireless systems.
Current system designs cannot support future mobile traffic.
Ideas:
  Throughput can be significantly increased by allowing
device-to-device communication.
  Exploit file popularity and caching capabilities.
With Device-to-Device Transmission
(Example Timeslot).

## Slide 4
User 1 Modes:
Automatic File Search
Browse a Neighbor
Browse a Social Group
User 1 Public Directory:
Music Videos
  Lady GaGa
YouTube Clips
Movies
  Bob the Builder
  Thomas the Train
User 2 Modes:
Automatic File Search
Browse a Neighbor
Browse a Social Group
User 2 Public Directory:
Music Videos
  Glee Clips
  Taylor Swift
YouTube Clips
  Clippers Highlights
CISS Talks
Neighbors are likely to have Popular Files.
Browsing capabilities induce popularity.
Example GUI at User Devices

## Slide 5
Peer-to-Peer Systems
Much prior work on internet peer-to-peer.
Much prior work on incentives (tokens, tit-for-tat, etc.)
[Neely, Golubchik Infocom 2011] considers utility optimization for general wireless peer-to-peer models, but:
  Requires coordination.
  Can have large delays in mobile network.
Current paper:
  Design for mobile setting with simplified coordination.
  Reduce Delays by opportunistically grabbing packets from
  current neighbors.
  To do this: We will treat a simplified model where each
  user only wants 1 “infinitely long” file.
  Prove optimality for the simplified model.
  Design a heuristic modification for more general systems.

## Slide 6
Simple Model: Network Structure
User devices (example: Handsets)
  Want data.
  Typically mobile.
  Have fewer files cached.
Access point devices (example: Basestations, Femto Nodes)
  Don’t want data
  Typically non-mobile
  Typically have access to many more files.
N Devices:
{Devices}
= {Users} U {Access Points}

## Slide 7
Simple Model: Transmission Options
1-Hop Networking (no relaying).
Access points can transmit to users.
Users can transmit to other users.
Time-Varying Channels, timeslots t in {0, 1, 2, …}.
ω(t) = “topology state” on slot t.
Slot t decision: Choose (μnk(t)) in R(ω(t)).
N Devices:
{Devices}
= {Users} U {Access Points}
Transmission matrix
Set of Options for slot t.
Example sub-cell structure: Decisions are distributed.

## Slide 8
Simple Model: File Requests and Availability
N Devices:
{Devices}
= {Users} U {Access Points}
Each user wants 1 file consisting of “infinite” # of packets.
Fk = {Devices that have the file that user k wants}.
Users grab packets of their desired file over time.
xk(t) = ∑a μak(t) = Total user k downloads on slot t.
yk(t) = ∑b μkb(t) = Total user k uploads on slot t.

## Slide 9
Stochastic Network Optimization Problem
xk = Time average rate of user k downloads.
yk = Time average rate of user k uploads.
Maximize: ∑k φk( xk )
Subject to:
(1) ακxκ ≤ βκ+ yκ for all users k
(2) (μnk(t)) in R(ω(t))
for all t in {0, 1, 2, …}
Concave utility
functions
Tit-for-Tat
constraints to
incentivize
participation

## Slide 10
Solution (Lyapunov Optimization)
ακxκ ≤ βκ+ yκ
Virtual queues Hk(t) for tit-for-tat constraints:
Hk(t+1) = max[Hk(t) + αkxk(t) – βk – yk(t), 0]
Hk(t)
αkxk(t)
βk + yk(t)
Hk(t) is a reputation queue:
Hk(t) low “good reputation”
Hk(t) high “bad reputation”

## Slide 11
Dynamic Algorithm
Maintain a request queue Qk(t) and reputation queue Hk(t).
User k request decision on slot t:
Maximize: Vφk(γk(t)) – Qk(t)γk(t)
Subject to: 0 ≤ γk(t) ≤ γmax
Transmission Decisions on slot t:
Maximize: ∑ μnk(t)Wnk(t)
Subject to: (μnk(t)) in R(ω(t))
Update Queues:
Qκ(t+1) = max[Qk(t) + γk(t) – xk(t), 0]
Hk(t+1) = max[Hk(t) + αkxk(t) – βk – yk(t), 0]

## Slide 12
What are the weights Wnk(t)?
Transmit decision: Maximize ∑ μnk(t)Wnk(t)
For users n and k:
Wnk(t) = Qk(t) + Hn(t) – αkHk(t)
“Differential Reputation”
Like “backpressure” with reputations!
The optimization naturally gives a “token”
mechanism: If your reputation is bad, you
need to improve it to get more downloads!

## Slide 13
Performance Theorem
For all sample paths of time-variation
(possibly non-ergodic topology states w(t)),
the queues Qk(t), Hk(t) are deterministically
bounded by O(V).
All tit-for-tat constraints are satisfied.
If w(t) is ergodic, then:
Achieved utility ≥ Optimal utility – O(1/V)

## Slide 14
Simulation Scenario
Base Station
1 Base Station, 50 mobile users.
Base station transmission is orthogonal from P2P.
P2P transmissions distributed over sub-cells.
1 P2P transmission per sub-cell.
Files randomly selected at time 0:
p = Pr[other user has file] = Availability probability

## Slide 15
New files chosen at beginning of each phase. Held fixed over 3 phases.
Phase 1: Availiability prob = 5%
Phase 2: Availability prob = 10%
Phase 3: Availability prob = 7%
(Even with p = 5%, the P2P traffic is more than twice the BS traffic!)

## Slide 16
New files chosen at beginning of each phase. Held fixed over 3 phases.
Phase 1: Availiability prob = 5%
Phase 2: Availability prob = 10%
Phase 3: Availability prob = 7%
(This and previous use V=10, a=0.5. Then Q(t) ≤ 12 packets for all t.)

## Slide 17
The above shows throughput versus V.
Different tit-for-tat parameters α are shown:
Larger α means more incentives to participate, but optimality is then
more constrained.

## Slide 18
The corresponding queue size for the same experiment as previous
slide.
Our analytical bound ensures Queue size ≤ V+2 for all time.
At V=10 (which gives near optimality from previous figure) we get
a queue bound of 12.

## Slide 19
Lyapunov optimization approach to wireless P2P scheduling.
“Backpressure” on Reputations.
P2P leads to significant gains in throughput.
Our algorithm, derived for the simple “infinite file size” assumption,
also works well on finite file sizes and non-ergodic events.
Conclusions
Base Station